## Slide 1: DIRECT DETECTION OF EXOPLANETS USING TUNABLE KERNEL-NULLING Vincent Foriel1,*, Frantz Martinache1, David Mary1 1 Université Côte d'Azur, Observatoire de la Côte d'Azur, CNRS, Laboratoire Lagrange, France * vincent.foriel@oca.eu
Distribution analysis 📊
By introducing input phase aberrations, the system is not able to perfectly cancel the star light. By multiplying the observation, we obtain such distribution:
The presence of an exoplanet in the field of view result in a shift of the distribution. The more the planet will be bright, the more the shift will be pronounced. In practice, both distribution are almost indistinguishable. We then test several estimators to retrieve the true value of the signal and then estimate the probability of detection.
Thermo-optic phase shifter 🌡️
Coming from telecom technologies, the thermo-optic phase shifters consist in heating a fiber core using an electrode in order to increase the optical index and then induce an artificial OPD. Thanks to the compactness of such systems, the heat transfert is fast enough to have response time of about . These shifters have been designed to work optimally at
In a nutshell 🥜
This thesis aim to enhance nulling interferometry for exoplanet detection using a four-telescope architecture named Kernel-Nuller. By integrating 14 active phase shifters, we aim to mitigate phase aberrations caused by manufacturing defects. An algorithm is developed to optimize device performance, validated through simulations and lab experiments. A second phase consist in analyzing intensity distributions produced by Kernel-Nuller and applying statistical tests and machine learning to extract science information. This poster present the preliminary results.
Calibration algorithm 🗜️
To find the best phase shifts to introduce, I proposed an algorithm inspired from dichotomy and gradient descent that accept or reject steps in the parameter space according to the bright and dark asymmetry metrics. and are respectively the bright and darks output intensities.
Parallactic diversity 🔄️
Taking advantage of the earth rotation, the kernel distribution will shift according to a known modulation. For each kernel output, one fit this modulation to the data points, giving the position and contrast of the potential object. By averaging all these parameter and computing a global fit, we can compare if this last one is well correlated to each kernel modulation.
Nulling interferometry 〰️ On the VLTI
This technique consist in taking advantage of the angular separation and the coherence properties of the light to destroy the star light and combine the planet light in the same process. Our approach
Enhance this principle by
Introducing « Kernels »
which combine the light
from 3 telescopes or more
to be less sensitive to low
order phase aberrations and
Asymmetries the output to
better constrain the planet
position.
Discussions & prospects 💬
These promising results are mitigated by the persistent sensibility to high order phase aberration. A contrast of require an AO correction that bring phase aberration below . Also, two of the main prospects will consist to make these simulations chromatic and confirm these results in a lab.
Active optical components 💡
The idea of our architecture is to combine the nulling interferometry with the phase shifter technologies to make an active optical component that can be calibrated to compensate the phase aberration induced by the manufacturing defects.
References 📜
Ref1
Ref2
Ref3
Ref4
Ref5
Acknowledgment 🤝
To acknowledge:
Project PHOTONICS
Romain Laugier – Wise advices & good intuitions to solve issues
Nick Cvetojevic – Explanations about kernel-nulling
Margaux Abello – Help on presentation & inspiration
Figure 2: Concept of nulling interferometry
Figure 4: Scheme of thermo-optic phase shifter
Figure 1: Scheme of our Kernel-Nulling architecture
Figure 5: Picture of the waffle that contain several prototype architectures of Kernel-Nuller. The overall component size is comparable to a 1 cent coin.
Figure 6: phase and amplitude of the 4 input signals oon the 6 dark outputs before and after the calibration process
Image reconstruction 🖼️
By weighting the kernel map by the output intensity and integrating it over the parallactic angle, we can retrieve which part of the sky has potentially contributed to this output. By cumulating the 3 probable intensity distribution, it is then possible to constrain precisely which part of the sky contributed the most, and then reveal the object!
Figure 3: Transmission map of one of the Kernels obtained using the 4 telescopes of the VLTI. The transmission zones and blind bands are directly derived from the UT position. By rotating the baseline, we can get a modulated signal from which we can precisely constrain the planet position.
Figure 7: Intensity distribution obtained on a kernel output
(with an extremely bright planet to clearly show the distribution shift)
Figure 8: ROC test to estimate the confidence of detection regarding to the probability of false alarm.
Figure 9: Kernel modulation & fiting
Figure 10: Repartition of probable contributions and cumulation of these maps to get a sort of reconstructed image.
Figure 11: Evolution of kernel distribution spread according to the input phase aberations.